## Slide 1: Microprocessors and Assembly Language Lecture 2 Hamed Farbeh farbeh@aut.ac.ir Spring 2023

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013
Design of Microprocessor-Based Systems (aka Embedded Systems Design and Implementation), Prabal Dutta, University of Michigan
CortexTM-M3 Revision r2p1 Technical Reference Manual
ARMv7-M Architecture Reference Manual

## Slide 3: Microcontrollers

## Slide 4: Microcontrollers
Bell’s Law: A new computer class every decade
“Roughly every decade a new, lower priced computer class forms based on a new programming platform, network, and interface resulting in new usage and the establishment of a new industry.”
- Gordon Bell [1972,2008]

## Slide 5: Microcontrollers: A Brief History
1980s and 1990s
  Intel: x86 (8088/86, 80286, 80386, 80486, and Pentium)
  Motorola (Freescale=>NXP): 68xxx (68000, 68010, 68020)
  High-end embedded systems (Cisco routers)
    Intel’s 32-bit x86
    Motorola’s 32-bit 68xxx
  Low-end embedded systems
    Intel’s 8-bit 8051
    Motorola’s 8-bit 68HC1

## Slide 6: Microcontrollers: A Brief History
Major players in the 8-bit market
  PIC from Microchip: 1976
  AVR from Atmel (Acquired by Microchip 2016): 1996
  Leaders in terms of volume (2013): PIC and AVR
    2019: Microchip and Renesas
Late 1990s
  ARM challenged Intel and Motorola in 32-bit market

## Slide 7: Microcontrollers: A Brief History
RISC features to enhance the performance, BUT
  Intel & Motorola: compatibility with legacy software
    Could not start over
    Massive amounts of gates to keep up the performance
      Increased power consumption of the x86
      Unacceptable for battery-powered embedded products
  ARM: A clean RISC architecture
    Leading microcontroller in the 32-bit market

## Slide 8: Currently Available Microcontrollers
32-bit
  ARM, AVR32 (Atmel), ColdFire (Freescale), MIPS32, PIC32 (Microchip), PowerPC, TriCore (Infineon), SuperH
16-bit
  MSP430 (TI), HCS12 (Freescale), PIC24 (Microchip), dsPIC (Microchip)
8-bit
  8051, AVR, HCS08 (Freescale), PIC16, PIC18

## Slide 9
Why study the ARM architecture?

## Slide 10: Lots of manufacturers ship ARM products

## Slide 11: Giant Partners

## Slide 12: ARM is the Big Player
ARM has a huge market share
2011: ARM has chips in 90% of the world’s mobile handsets
2010: ARM has chips in 95% of the smartphone market
  And, 10% of the notebook market
    Expected to hit 40% of the notebook market in 2015 (?)
Heavy use in general embedded systems
  Cheap to use
  Flexible

## Slide 13: A Brief History of the ARM
Came out of a company called Acorn Computers
  In United Kingdom in the 1980s
  Prof. Steve Furber of Manchester Univ. and Sophie Wilson
    Define the ARM architecture and instructions
  First ARM chip: 1985
    Acorn RISC Machine (ARM)
    Produced by VLSI Technology Corp.
    World’s First commercial RISC processor
    Unable to compete with x86 (8088, 80286, 80386, …) PCs from IBM and other personal computer makers

## Slide 14: A Brief History of the ARM
    Acorn was forced to push ARM into emb. market
Apple Corp.
  Using the ARM chip for the PDA (personal digital assistants) products
ARM as a new company
  ARM (Advanced RISC Machine)
  A big gamble
    Selling the rights to this new CPU to other silicon
    manufacturers and design houses

## Slide 15: ARM Company Milestones
    1982: Acorn produced a computer for BBC
    1983: Acorn began designing its own uP
    1985: ARMv1 developed (2500 trans., 4MHz)
    1990: Advanced RISC Machines (ARM) spins out
    1992: GEC Plessey and Sharp licensed ARM
    1993: Texas Instrument licensed ARM
    1995: ARM lunched Software Development Toolkit
    1996: ARM and MS worked together: Windows CE on ARM
    1997: Hyundai, Lucent, Philips, Rockwell, and Sony licensed ARM

## Slide 16: ARM Company Milestones
    1998: HP, IBM, Matsushita, Seiko Epson, and Qualcomm licensed ARM
    1999: LSI Logic, STMicroelectronics, and Fujitsu licensed ARM
    2000: Agilent, Altera, Micronas, Mitsubishi, Motorola, Sanyo, Triscend and ZTEIC licensed ARM
    2001: Global UniChip, Samsung and Zeevo licensed ARM
      Share of the 32-bit embedded RISC microprocessor market: 76.8%
    2002: Seagate, Broadcom, Philips, Matsushita, Micrel, eSilicon, Chip Express and ITRI licensed ARM
    2004: The ARM Cortex family of processors was announced (Cortex-M3)
    2005: ARM acquired Keil Software
    2009: ARM launches its smallest, lowest power, most energy efficient processor: Cortex-M0
    ….

## Slide 17
    Making money from selling IP (intellectual property)
    has made ARM one of the most widely used
    CPU architectures in the world

## Slide 18: ARM Family Variations

## Slide 19: ARM: One CPU, Many Peripherals
    ARM Defines and holds the copyright to
      Details of arch., reg., intr. set, memory map, and timing
        For the ARM CPU
    Design houses and semiconductor manufacturers
      Add their own peripherals
        I/O ports, serial port UART, timers, ADC, SPI, DAC, I2C, …
    Same instructions and architecture, different peripherals
      Incompatibility across vendors
    Keil IDE: provides peripheral libraries for chips from various vendors

## Slide 20: ARM Simplified Block Diagram