## Slide 1: Microprocessors and Assembly Language Lecture 21 Hamed Farbeh farbeh@aut.ac.ir Spring 2023

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013

## Slide 3: Signed Integer Numbers Arithmetic

## Slide 4
Signed number
Loading a signed byte
    ; assume memory location 0x80000 contains -2 = 1111 1110 and R1=0x80000
    LDRB R0, [R1] ; now R0 = 0000 0000 0000 0000 0000 0000 1111 1110 = 254
LDRB zero-extends the loaded byte to fit 32 bits
We need to sign-extend it

## Slide 5
Signed number
Sign extension and avoiding erroneous results
    ; assume memory location 0x80000 has +96 = 0110 0000 and R1=0x80000
    LDRSB R0, [R1] ; R0 = 0000 0000 0000 0000 0000 0000 0110 0000
    ; assume memory location 0x80000 contains -2 = 1111 1110 and R2=0x80000
    LDRSB R4, [R2] ; R4 = 1111 1111 1111 1111 1111 1111 1111 1110
    ; assume 0x80000 contains +260 = 0000 0001 0000 0100 and R1=0x80000
    LDRSH R0, [R1] ; R0=0000 0000 0000 0000 0000 0001 0000 0100
    ; assume location 0x20000 has -327660=0x8002 and R2=0x20000
    LDRSH R1, [R2] ; R1=FFFF8002

## Slide 6
Signed number
Signed number multiplication: SMULL
    LDR R1, =-3500 ; R1 = -3500 (0xFFFFF254)
    LDR R0, =-100 ; R0 = -100 (0xFFFFFF9C)
    SMULL R2, R3, R0, R1
Signed number comparison
    CMP Rn, Op2
    Op2 > Rn → V = N Op2 = Rn → Z = 1 Op2 < Rn → N ≠ V

## Slide 7
Signed number
Signed comparison condition codes
Condition Code | Action | Flags
MI | Negative | N=1
PL | Positive or zero | N=0
VS | Overflow | V=1
VC | No overflow | V=0
GE | Signed greater than or equal | N = V
LT | Signed less than | N != V
GT | Signed greater than | Z=0 & N=V
LE | Signed less than or equal | Z=1 or N != V

## Slide 8
Signed number
ASR (arithmetic shift right)
    MOV Rn, Op2, ASR count
    or
    ASR Rn, Op2, count

## Slide 9
Question
An array of 32-bit non-zero signed integers start from memory address 0x80000. We don’t know the size of the array but we do know that the array is terminated with a zero after the last element. Write a program to loop through and find the minimal element of the array.
0x80000 | 0x80004 | … | Last element | Terminal element
1200 | -54 | … | 202 | 0

## Slide 10: End of Chapter 5!