## Slide 1: Electrical Circuits Lecture 15: BJT Transistors By: Mahmoud Momtazpour ceit.aut.ac.ir/~momtazpour
Amirkabir University of Technology

## Slide 2: Topic Overview
BJT Large Signal Model
BJT Modes of Operations
BJT DC Analysis
BJT Small Signal Model
BJT AC Analysis

## Slide 3: BJT
B: Base
C: Collector
E: Emitter
Notes: BJT یک نوع ترانزیستور است که در آن، یک جریان کم در بیس، یک جریان زیاد در کالکتور ایجاد می کند و همین می تواند مبنای تقویت کنندگی باشد.
آیا می توان با اتصال دو عدد دیود با سیم، یک ترانزیستور ساخت؟ خیر! لایه بیس باید خیلی نازک و بین دو دیود مشترک باشد تا بتوان جریان کم در بیس را به جریان زیاد در کلکتور تبدیل کرد.
همچنین این المان به دلیل ساختارش نامتقارن است و جای کالکتور و امیتر مشخص و ثابت است. ناحیه امیتر دارای سطح کوچکتری است و غلظت ناخالصی آن نیز بسیار بیشتر از کالکتور است.

## Slide 4: BJT Operation

## Slide 5: BJT Large Signal Model
Ebers-Moll Model
Modes of operation:
  Cut-off
  Forward Active
  Reverse Active
  Saturation
NPN:
PNP:

## Slide 6: NPN BJT Modes of Operation
Cut-off

## Slide 7: NPN BJT Modes of Operation
Forward Active
Acts as an amplifier!

## Slide 8: NPN BJT Modes of Operation
Reverse Active
The collector diode is built in a way that it can tolerate large reverse biases, but emitter diode can’t.
It also has poor
So, we usually don’t use BJTs in this mode…

## Slide 9: NPN BJT Modes of Operation
Saturation
Acts as a switch!
0.2 is called Vsat
  (IC is set by the circuit, not by IB)

## Slide 10: BJT Configurations
Common Base
Common Collector
Common Emitter

## Slide 11: BJT DC Analysis
Write BE and CE KVLs
Assume Cut-off (), use BE-KVL to find :
  If OK! Use CE-KVL to find .
  If , assumption is not true…
Assume Active (), assume , use BE-KVL to find Find . Use CE-KVL to find .
  If , OK! Otherwise, assumption is not true
Assume Saturation (). Use CE-KVL to find . Double Check

## Slide 12: Example
Find ()
Write BE and CE KVLs:
Assume Cut-off
Assume Active