## Slide 1: Comparator

## Slide 2: Two-Bit Comparator
we'll need a 4-variable Karnaugh map for each of the 3 output functions
block diagram
LT EQ GT
A B < C D A B = C D A B > C D
A
B
C
D
N1
N2
A B C D LT EQ GT
0 0 0 0 0 1 0
0 1 1 0 0
1 0 1 0 0
1 1 1 0 0
0 1 0 0 0 0 1
0 1 0 1 0
1 0 1 0 0
1 1 1 0 0
1 0 0 0 0 0 1
0 1 0 0 1
1 0 0 1 0
1 1 1 0 0
1 1 0 0 0 0 1
0 1 0 0 1
1 0 0 0 1
1 1 0 1 0
and
truth table

## Slide 3: Two-Bit Comparator (cont’d)
A' B' D + A' C + B' C D
B C' D' + A C' + A B D'
LT =
EQ =
GT =
K-map for EQ
K-map for LT
K-map for GT
0 0
1 0
0 0
0 0
D
A
1 1
1 1
0 1
0 0
B
C
1 0
0 1
0 0
0 0
D
A
0 0
0 0
1 0
0 1
B
C
0 1
0 0
1 1
1 1
D
A
0 0
0 0
0 0
1 0
B
C
= (A xnor C) • (B xnor D)
A'B'C'D' + A'BC'D + ABCD + AB'CD’

## Slide 4: Equality Comparator
XNOR
X
Y
Z
Z = X XNOR Y
X Y Z
0 0 1
0 1 0
1 0 0
1 1 1

## Slide 5: 4-bit Equality Detector
Equality
Detector
A[3..0]
B[3..0]
A_EQ_B

## Slide 6: 4-Bit Equality Comparator
A0
A1
A2
A3
B0
B1
B2
B3
A_EQ_B
C0
C1
C3
C2

## Slide 7: 4-bit Magnitude Comparator
Magnitude
Detector
A[3..0]
B[3..0]
A_EQ_B
A_LT_B
A_GT_B

## Slide 8: Magnitude Comparator
How can we find A_GT_B?
How many rows would a truth table have?
28 = 256!

## Slide 9: Magnitude Comparator
If A = 1001 and
B = 0111
is A > B?
Why?
Find A_GT_B

## Slide 10: Magnitude Comparator
If A = 1001 and
B = 0111
is A > B?
Why?
Because A3 > B3
i.e. A3 . B3’ = 1
Therefore, one term in the
logic equation for A_GT_B is
A3 . B3’
Find A_GT_B

## Slide 11: Magnitude Comparator
If A = 1101 and
B = 1011
is A > B?
Why?
Because A3 = B3 and
A2 > B2
i.e. C3 = 1 and
A2 . B2’ = 1
A_GT_B = A3 . B3’
+ …..

## Slide 12: Magnitude Comparator
If A = 1101 and
B = 1011
is A > B?
Why?
Because A3 = B3 and
A2 > B2
i.e. C3 = 1 and
A2 . B2’ = 1
Therefore, the next term in the
logic equation for A_GT_B is
C3 . A2 . B2’
A_GT_B = A3 . B3’
+ …..

## Slide 13: Magnitude Comparator
If A = 1010 and
B = 1001
is A > B?
Why?
Because A3 = B3 and
A2 = B2 and
A1 > B1
i.e. C3 = 1 and C2 = 1 and
A1 . B1’ = 1
Therefore, the next term in the
logic equation for A_GT_B is
C3 . C2 . A1 . B1’
A_GT_B = A3 . B3’
+ C3 . A2 . B2’
+ …..

## Slide 14: Magnitude Comparator
If A = 1011 and
B = 1010
is A > B?
Why?
Because A3 = B3 and
A2 = B2 and
A1 = B1 and
A0 > B0
i.e. C3 = 1 and C2 = 1 and
C1 = 1 and A0 . B0’ = 1
Therefore, the last term in the
logic equation for A_GT_B is
C3 . C2 . C1 . A0 . B0’
A_GT_B = A3 . B3’
+ C3 . A2 . B2’
+ C3 . C2 . A1 . B1’
+ …..

## Slide 15: Magnitude Comparator
A_GT_B = A3 . B3’
+ C3 . A2 . B2’
+ C3 . C2 . A1 . B1’
+ C3 . C2 . C1 . A0 . B0’

## Slide 16: Magnitude Comparator
A_LT_B = A3’ . B3
+ C3 . A2’ . B2
+ C3 . C2 . A1’ . B1
+ C3 . C2 . C1 . A0’ . B0
Find A_LT_B

## Slide 17: TTL 74x85
4
4
B
A
g
e
l
gt
eq
lt

## Slide 18: TTL 74x85
  if (A>B) lt=0, eq=0, gt=1
  if (A<B) lt=1, eq=0, gt=0
  if (A=B) lt=l, eq=e, gt=g
  The three l, e and g inputs are used when cascading.
4
4
B
A
g
e
l
gt
eq
lt

## Slide 19: Comparator (continued…)
  Let us now cascade four of the 74x85 to construct a 16 bit comparator.
Exercise: Analyze it.

## Slide 20: TTL 74x682
  8-bit Comparator
    Arithmetic conditions derived from 74x682 outputs?
    And their circuits?

## Slide 22: Maximum Finder
Design a maximum finder
a
b
4
4

## Slide 23: Maximum Finder
Design a maximum finder