## Slide 1: Hardware Description Language
HDL

## Slide 2: Hardware Description Language
HDL
  Describes circuits and systems in text.
    As a software program.
  Can be processed by computers.
  VHDL, Verilog, AHDL, SystemC.
Applications:
  Simulation
  Synthesis

## Slide 3: Simulation and Synthesis
Simulation
  Input waveform and circuit description --> Output waveform
  Predicts circuit behavior before fabrication (debug before physical implementation).
کامپايل
اجرا
برنامه نويسي
ويرايش

## Slide 4: Simulation and Synthesis
Synthesis
  Automatic design.
  Software program takes design description and tries to find the circuit
کامپايل
شبيه سازي
ورود طرح
ويرايش
سنتز
شبيه سازي
ويرايش

## Slide 5: Verilog HDL
  Verilog or VHDL?
    Similar concepts, different syntax
  Similar to C/C++ Syntax
    Case sensitive,
    Comments: //
    ; at the end of each statement

## Slide 6: Example
module:
  Hardware component
Ports:
  As function parameters
    But must specify input or output
wire:
  Intermediate signals
//HDL Example 3-1
//--------------------------
module smpl_circuit(A,B,C,x,y);
input A,B,C;
output x,y;
wire e;
and g1(e,A,B);
not g2(y, C);
or g3(x,e,y);
endmodule
Concurrent Execution
  Order not important.

## Slide 7: Example
//HDL Example 3-1
//--------------------------
module smpl_circuit(A,B,C,x,y);
input A,B,C;
output x,y;
wire e;
and g1(e,A,B);
not g2(y, C);
or g3(x,e,y);
endmodule
Concurrent Execution
  Order not important.

## Slide 8: Delays
Timescale:
  ‘timescale 1ns/100ps
    1ns: time unit
    100ps: precision (unit used for rounding)
    Default: 1ns/100ps (0.1 ns)
Gate Delays:
  Used by simulator to generate correct waveforms

## Slide 9: Delays
//HDL Example 3-2
//---------------------------------
//Description of circuit with delay
module circuit_with_delay (A,B,C,x,y);
input A,B,C;
output x,y;
wire e;
and #(30) g1(e,A,B);
or #(20) g3(x,e,y);
not #(10) g2(y,C);
endmodule

## Slide 10: Testbench
Testbench:
  Program written to test the circuit
  Sets the input values,
    Changes them over time.
  Instantiates the module(s).
  Inputs by reg (generally in sequential constructs)
  Outputs by wire

## Slide 11: Testbench Example
Testbench:
  Doesn’t have port.
  Instantiation.
  <size>’<base><value>
    Base: b, o, d, h
    32’d87
  ABC = “000”  “111”
  100ns delay.
  Finishes at 200ns.
//HDL Example 3-3
//----------------------
//Stimulus for simple circuit
module stimcrct;
reg A,B,C;
wire x,y;
circuit_with_delay cwd(A,B,C,x,y);
initial
begin
A = 1'b0; B = 1'b0; C = 1'b0;
#100
A = 1'b1; B = 1'b1; C = 1'b1;
#100 $finish;
end
endmodule
//Description of circuit with delay
module circuit_with_delay (A,B,C,x,y);
input A,B,C;
output x,y;
wire e;
and #(30) g1(e,A,B);
or #(20) g3(x,e,y);
not #(10) g2(y,C);
endmodule

## Slide 12: Testbench Example

## Slide 13: Boolean Expressions
  & AND
  | OR
  ~ NOT
    assign x = (A & B) | ~C;
//HDL Example 3-4
//------------------------------
//Circuit specified with Boolean equations
module circuit_bln (x,y,A,B,C,D);
input A,B,C,D;
output x,y;
assign x = A | (B & C) | (~B & C);
assign y = (~B & C) | (B & ~C & ~D);
endmodule

## Slide 14: Primitives
Built-in Primitives:
  and, or, not, nand, nor, xor, xnor, buf.
User-Defined Primitives (UDP):
  User can define by truth table.

## Slide 15: Primitives
User-Defined Primitives (UDP):
  User can define by truth table.
  Use primitive keyword (instead of module)
  Only one output but many inputs
    first output, then inputs
  Inputs’ order must correspond with the truth table.
  Truth table between table and end table.

## Slide 16: UDP
//HDL Example 3-5
//-----------------------------------
//User defined primitive(UDP)
primitive crctp (x,A,B,C);
output x;
input A,B,C;
//Truth table for x(A,B,C) = Minterms (0,2,4,6,7)
table
// A B C : x (Note that this is only a comment)
0 0 0 : 1;
0 0 1 : 0;
0 1 0 : 1;
0 1 1 : 0;
1 0 0 : 1;
1 0 1 : 0;
1 1 0 : 1;
1 1 1 : 1;
endtable
endprimitive

## Slide 17: UDP Usage
  Usage: much the same way as a system-defined primitives:
crctp #(20) myInstance(w, x, y, z);

## Slide 18: Simulation
ModelSim:
  An industrial and widely used simulator
  $25K