## Slide 1: اعمال رياضی با اعداد

## Slide 2: اعمال رياضي باينري: جمع
قوانين: مانند جمع دسيمال
با اين تفاوت که 1+1 = 10  توليد نقلي
  0+0 = 0(c0) (sum 0 with carry 0)
  0+1 = 1+0 = 1(c0)
  1+1 = 0(c1)
  1+1+1 = 1(c1)

## Slide 3: اعمال رياضي باينري: جمع
قوانين: مانند جمع دسيمال
با اين تفاوت که 1+1 = 10  توليد نقلي
  0+0 = 0(c0) (sum 0 with carry 0)
  0+1 = 1+0 = 1(c0)
  1+1 = 0(c1)
  1+1+1 = 1(c1)
Carry | 1 | 1 | 1 | 1 | 1 | 0
Augend | 0 | 0 | 1 | 0 | 0 | 1
Addend | 0 | 1 | 1 | 1 | 1 | 1
Result | 1 | 0 | 1 | 0 | 0 | 0

## Slide 4: سرريز (Overflow)
  اگر تعداد بيت ها = n و حاصل جمع n+1 بيت نياز داشته باشد
     سرريز

## Slide 5: اعمال رياضي باينري: تفريق
قوانين:
  0-0 = 1-1 = 0 (b0) (result 0 with borrow 0)
  1-0 = 1 (b0)
  0-1 = 1 (b1)
  …
Borrow | 1 | 1 | 0 | 0 | 
Minuend | 1 | 1 | 0 | 1 | 1
Subtrahend | 0 | 1 | 1 | 0 | 1
Result | 0 | 1 | 1 | 1 | 0

## Slide 6: روش انجام محاسبات
  الگوريتم هاي اعمال رياضي مبناي 10 را به خاطر آوريد.
  آنها را براي مبناي مورد نظر تعميم دهيد.
  قانون مبناي مورد نظر را به کار بريد.
    براي باينري: 1+1=10

## Slide 7: نمايش اعداد
نمايش اعداد مثبت:
  در بيشتر سيستم ها يکسان است.
نمايش اعداد منفي:
  اندازه-علامت (Sign magnitude)
  مکمل 1 (Ones complement)
  مکمل 2 (Twos complement)
    در بيشتر سيستم ها: مکمل 2
فرض:
  ماشين با کلمه هاي 4 بيتي:
     16 مقدار مختلف قابل نمايش.
    تقريباً نيمي مثبت، نيمي منفي.

## Slide 8: نمايش اعداد
اندازه-علامت:
High order bit is sign: 0 = positive (or zero), 1 = negative
Three low order bits show the magnitude: 0 (000) thru 7 (111)
Number range for n bits = [-(2 n-1 -1), +(2 n-1 -1)]
Two representations for 0
Cumbersome addition/subtraction
Must compare magnitudes to determine sign of result

## Slide 9: نمايش اعداد
مکمل 1:
N is positive number, then N is its negative 1's complement
N = (2 - 1) - N
n
Example: 1's complement of 7

## Slide 10: نمايش اعداد
مکمل 1:
N is positive number, then N is its negative 1's complement
N = (2 - 1) - N
n
Example: 1's complement of 7
2 = 10000
-1 = 00001
1111
-7 = 0111
1000
= -7 in 1's comp.
Shortcut method:
simply compute bitwise complement
0111 -> 1000
4

## Slide 11: نمايش اعداد
مکمل 1:
Subtraction implemented by addition & 1's complement
Still two representations of 0! This causes some problems
Some complexities in addition

## Slide 12: نمايش اعداد
مکمل 2:
Only one representation for 0
One more negative number than positive number
like 1's comp
except shifted
one position
clockwise

## Slide 13: نمايش اعداد
مکمل 2:
N* = 2 - N
n
Example: Twos complement of 7

## Slide 14: نمايش اعداد
مکمل 2:
N* = 2 - N
n
Example: Twos complement of 7
2 = 10000
7 = 0111
1001 = repr. of -7
4
sub

## Slide 15: نمايش اعداد
مکمل 2:
N* = 2 - N
n
Example: Twos complement of 7
2 = 10000
7 = 0111
1001 = repr. of -7
Example: Twos complement of -7
4
sub

## Slide 16: نمايش اعداد
مکمل 2:
N* = 2 - N
n
Example: Twos complement of 7
2 = 10000
7 = 0111
1001 = repr. of -7
Example: Twos complement of -7
4
2 = 10000
-7 = 1001
0111 = repr. of 7
4
sub
sub

## Slide 17: نمايش اعداد
مکمل 2:
N* = 2 - N
n
Example: Twos complement of 7
2 = 10000
7 = 0111
1001 = repr. of -7
Example: Twos complement of -7
4
2 = 10000
-7 = 1001
0111 = repr. of 7
4
sub
sub
Shortcut method:
Twos complement = bitwise complement + 1
0111 -> 1000 + 1 -> 1001 (representation of -7)
1001 -> 0110 + 1 -> 0111 (representation of 7)

## Slide 18: مکمل 2
Here’s an easier way to compute the 2’s complement:
  Leave all least significant 0’s and first 1 unchanged.
  Replace 0 with 1 and 1 with 0 in all remaining higher significant bits.
Examples:
  N = 1010 N = 01011000

## Slide 19: مکمل 2
Here’s an easier way to compute the 2’s complement:
  Leave all least significant 0’s and first 1 unchanged.
  Replace 0 with 1 and 1 with 0 in all remaining higher significant bits.
Examples:
  N = 1010 N = 01011000 01 10 10101000
  2’s complement 2’s complement
unchanged
complement
unchanged
complement

## Slide 20: جمع و تفريق مکمل 2
4
+ 3
7
-4
+ (-3)
-7
4
- 3
1
-4
+ 3
-1
Simpler addition scheme makes twos complement the most common
choice for integer number systems

## Slide 21: جمع و تفريق مکمل 2
4
+ 3
7
0100
0011
0111
-4
+ (-3)
-7
1100
1101
11001
4
- 3
1
0100
1101
10001
-4
+ 3
-1
1100
0011
1111
Simpler addition scheme makes twos complement the most common
choice for integer number systems

## Slide 22: جمع و تفريق مکمل 2
Why can the carry-out be ignored?
-M + N when N > M:
M* + N = (2 - M) + N = 2 + (N - M)
n
n
Ignoring carry-out is just like subtracting 2
n

## Slide 23: جمع و تفريق مکمل 2
Why can the carry-out be ignored?
-M + N when N > M:
M* + N = (2 - M) + N = 2 + (N - M)
n
n
Ignoring carry-out is just like subtracting 2
n
After ignoring the carry, this is just the right twos compl.
representation for -(M + N)
or (M+N)*
-M + -N where N + M < or = 2
n-1
-M + (-N) = M* + N* = (2 - M) + (2 - N)
= 2 - (M + N) + 2
n
n
n
n

## Slide 24: سرريز
Overflow Conditions
Add two positive numbers to get a negative number
or two negative numbers to get a positive number
5 + 3 = -8
-7 - 2 = +7
0000
0001
0010
0011
1000
0101
0110
0100
1001
1010
1011
1100
1101
0111
1110
1111
+0
+1
+2
+3
+4
+5
+6
+7
-8
-7
-6
-5
-4
-3
-2
-1
0000
0001
0010
0011
1000
0101
0110
0100
1001
1010
1011
1100
1101
0111
1110
1111
+0
+1
+2
+3
+4
+5
+6
+7
-8
-7
-6
-5
-4
-3
-2
-1

## Slide 25: سرريز
Overflow Conditions
5
3
-8
0 1 0 1
0 0 1 1
Overflow
-7
-2
7
1 0 0 1
1 1 1 0
Overflow
5
2
7
0 1 0 1
0 0 1 0
No overflow
-3
-5
-8
1 1 0 1
1 0 1 1
No overflow

## Slide 26: سرريز
Overflow Conditions
5
3
-8
0 1 1 1
0 1 0 1
0 0 1 1
1 0 0 0
Overflow
-7
-2
7
1 0 0 0
1 0 0 1
1 1 1 0
1 0 1 1 1
Overflow
5
2
7
0 0 0 0
0 1 0 1
0 0 1 0
0 1 1 1
No overflow
-3
-5
-8
1 1 1 1
1 1 0 1
1 0 1 1
1 1 0 0 0
No overflow
Method 1: Overflow when carry in to sign ≠ carry out
Method 2: Overflow when sign(A) = sign(B) ≠ sign (result)

## Slide 28: ضرب باينري
Shift-and-add algorithm, as in base 10
Check: 13 * 6 = 78
M’cand | 0 | 0 | 0 | 1 | 1 | 0 | 1
M’plier | 0 | 0 | 0 | 0 | 1 | 1 | 0
(1) |  |  | 0 | 0 | 0 | 0 | 0
(2) |  | 0 | 1 | 1 | 0 | 1 | 
(3) | 0 | 1 | 1 | 0 | 1 |  | 
Sum | 1 | 0 | 0 | 1 | 1 | 1 | 0

## Slide 29: Binary-Coded Decimal (BCD)
  A decimal code: Decimal numbers (0..9) are coded using 4-bit distinct binary words
  Observe that the codes 1010 .. 1111 (decimal 10..15) are NOT represented (invalid BCD codes)

## Slide 30: Binary-Coded Decimal
To code a number with n decimal digits, we need 4n bits in BCD
e.g. (365)10 = (0011 0110 0101)BCD
This is different from converting to binary, which is (365)10 = (101101101)2
Clearly, BCD requires more bits. BUT, it is easier to understand/interpret

## Slide 31: Application

## Slide 32: BCD Addition
Case 1:
Case 2:
Case 3:
0001 1
0101 5
(0) 6
0110 6
0101 5
(1) 1
1000 8
1001 9
(1) 7

## Slide 33: BCD Addition
Case 1:
Case 2:
Case 3:
0001 1
0101 5
(0) 0110 (0) 6
0110 6
0101 5
(0) 1011 (1) 1
1000 8
1001 9
(1) 0001 (1) 7
WRONG!
Note that for cases 2 and 3, adding a factor of 6 (0110) gives us the correct result.

## Slide 34: BCD Addition (cont.)
BCD addition is therefore performed as follows
  1) Add the two BCD digits together using normal binary addition
  2) Check if correction is needed
    a) 4-bit sum is in range of 1010 to 1111
    b) carry out of MSB = 1
  3) If correction is required, add 0110 to 4-bit sum to get the correct result;
   BCD carry out = 1

## Slide 35: BCD Addition (cont.)
Example: Add 448 and 489 in BCD.
  0100 0100 1000 (448 in BCD)
  0100 1000 1001 (489 in BCD)

## Slide 36: BCD Addition (cont.)
Example: Add 448 and 489 in BCD.
  0100 0100 1000 (448 in BCD)
  0100 1000 1001 (489 in BCD)
  10001 (greater than 9, add 6)
  10111 (carry 1 into middle digit)
  1101 (greater than 9, add 6)
10011 (carry 1 into leftmost digit)
  1001 0011 0111 (BCD coding of 93710)
0110
0110

## Slide 37: BCD Negative Number Representation
Similar to binary negative number representation but for r = 10.
  BCD 9’s complement
    invert each BCD digit (09, 1  8, 2  7,3  6, …7  2, 8  1, 9  0)
  BCD 10’s complement
    -N  10n - N; 9’s complement + 1

## Slide 38: Excess-3
مانند BCD ولي هر رقم +3
  جمع سرراست تر
  self-comlpement code
    (مکمل هر رقم = مکمل 9 آن)

## Slide 39: ASCII character code
  We also need to represent letters and other symbols  alphanumeric codes
  ASCII = American Standard Code for Information Interchange. Also known as Western European
  It contains 128 characters:
    94 printable ( 26 upper case and 26 lower case letters, 10 digits, 32 special symbols)
    34 non-printable (for control functions)
  Uses 7-bit binary codes to represent each of the 128 characters

## Slide 40: ASCII Table
Bell
Tab
Line Fd
Crg Ret
Null
BkSpc
Space
Escape

## Slide 41: ASCII Control Codes

## Slide 42: Unicode
  Established standard (16-bit alphanumeric code) for international character sets
  Since it is 16-bit, it has 65,536 codes
  Represented by 4 Hex digits
  ASCII is between 000016 .. 007B16

## Slide 43: Unicode Table
http://www.unicode.org/charts/

## Slide 44: Unicode
062B 1579 | ث | 062C 1580 | ج | 062D 1581 | ح | 062E 1582 | خ
0633 1587 | س | 0634 1588 | ش | 0635 1589 | ص | 0636 1590 | ض
063B 1595 | ػ | 063C 1596 | ؼ | 063D 1597 | ؽ | 063E 1598 | ؾ
0643 1603 | ك | 0644 1604 | ل | 0645 1605 | م | 0646 1606 | ن
064B 1611 | ً | 064C 1612 | ٌ | 064D 1613 | ٍ | 064E 1614 | َ
0653 1619 | ٓ | 0654 1620 | ٔ | 0655 1621 | ٕ | 0656 1622 | ٖ
065B 1627 | ٛ | 065C 1628 | ٜ | 065D 1629 | ٝ | 065E 1630 | ٞ
0663 1635 | ٣ | 0664 1636 | ٤ | 0665 1637 | ٥ | 0666 1638 | ٦
066B 1643 | ٫ | 066C 1644 | ٬ | 066D 1645 | ٭ | 066E 1646 | ٮ
0673 1651 | ٳ | 0674 1652 | ٴ | 0675 1653 | ٵ | 0676 1654 | ٶ
067B 1659 | ٻ | 067C 1660 | ټ | 067D 1661 | ٽ | 067E 1662 | پ
0683 1667 | ڃ | 0684 1668 | ڄ | 0685 1669 | څ | 0686 1670 | چ
068B 1675 | ڋ | 068C 1676 | ڌ | 068D 1677 | ڍ | 068E 1678 | ڎ

## Slide 45: ASCII Parity Bit
  Parity coding is used to detect errors in data communication and processing
    An 8th bit is added to the 7-bit ASCII code
  Even (Odd) parity: set the parity bit so as to make the # of 1’s in the 8-bit code even (odd)

## Slide 46: ASCII Parity Bit (cont.)
For example:
  Make the 7-bit code 1011011 an 8-bit even parity code  11011011
  Make the 7-bit code 1011011 an 8-bit odd parity code  01011011
Error Checking:
  Both even and odd parity codes can detect an odd number of error.
    An even number of errors goes undetected.

## Slide 47: Gray Codes
Gray codes are minimum change codes
  From one numeric representation to the next, only one bit changes
  Applications:
    Later.

## Slide 48: Gray Codes (cont.)
Binary
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Gray
0000
0001
0011
0010
0110
0111
0101
0100
1100
1101
1111
1110
1010
1011
1001
1000
Binary
00
01
10
11
Gray
00
01
11
10
Binary
000
001
010
011
100
101
110
111
Gray
000
001
011
010
110
111
101
100